## Slide 1: Industrial Facility Site Inspections
What to expect, look for & document
To play this presentation and hear the embedded audio, press “F5” from any Windows computer.

## Slide 2: How to view our webinar series
A pre-recorded version of this presentation will be available at: www.okc.gov/departments/public-works/divisions/storm-water-quality/storm-water-quality-workshops after the live event.
  Shortcut: www.okc.gov/swq then go to Storm Water Quality Workshops
All webinars in this series will be at this website, for playback any time.

## Slide 3: Objectives
Topics to be covered in this webinar:
  Industrial Stormwater & MSGP defined
  Requirements regarding site inspections
    EPA MSGP
    OKR05 (Oklahoma MSGP)
    Frequency
    Sector-Specific requirements
  Site inspection documentation
  General Guideline for site inspections
  Site examples of what to look for
  Record retention
  DEQ FAQ’s

## Slide 4: Industrial Stormwater & MSGP Defined

## Slide 5: What is Industrial stormwater?
Industrial stormwater is runoff from precipitation (rain, snow, sleet, freezing rain, or hail) that lands on industrial sites (e.g. manufacturing facilities, mines, airports).
  This runoff is often polluted by materials that are handled or stored on the sites, and the facilities are subject to regulations to control the discharges.
In the United States, facilities that discharge industrial stormwater to surface waters must obtain a permit under the National Pollutant Discharge Elimination System (NPDES), pursuant to the Clean Water Act.
  Stormwater permit regulations issued by the United States Environmental Protection Agency (EPA) govern the permit process.
Source: www.en.wikipedia.org/wiki/Industrial_stormwater

## Slide 6: What is an Industrial MSGP?
EPA published its Multi-Sector General Permit (MSGP) initially in 1995 to govern how industrial stormwater should be managed, and periodically it has updated and reissued the permit.
  The 2015 MSGP covers 29 industrial and commercial sectors (business types).
MSGPs are designed to cover multiple business types, in lieu of each business obtaining individual NPDES permits.
  For businesses that are required to obtain permits (i.e., businesses in one of the 29 covered Sectors), if the facility does not qualify for coverage under the MSGP, an individual permit is required.
State-issued general permits often include the same requirements as EPA's permit, but some states have additional requirements.
Source: www.en.wikipedia.org/wiki/Industrial_stormwater

## Slide 7: The 29 Industrial and Commercial Sectors
Timber Products Facilities (including wood preservation)
Paper and Allied Products Manufacturing Facilities
Chemical and Allied Products Manufacturing and Refining
Asphalt Paving and Roofing Materials and Manufacturers and Lubricant Manufacturers
Glass, Clay, Cement, Concrete, and Gypsum Product Manufacturing Facilities
Primary Metals Facilities
Metal Mining (Ore Mining and Dressing) Facilities
Coal Mines and Coal Mining-Related Facilities
Source: www.en.wikipedia.org/wiki/Industrial_stormwater

## Slide 8: The 29 Industrial and Commercial Sectors, continued
Oil and Gas Extraction Facilities
Mineral Mining and Processing Facilities
Hazardous Waste Treatment, Storage, or Disposal Facilities
Landfills and Land Application Sites
Automobile Salvage Yards
Scrap Recycling and Waste Recycling Facilities
Steam Electric Power Generating Facilities, including Coal Handling Areas
Motor Freight Transportation Facilities, Passenger Transportation Facilities, Petroleum Bulk Oil Stations and Terminals, Rail Transportation Facilities, and United States Postal Service Transportation Facilities
Source: www.en.wikipedia.org/wiki/Industrial_stormwater

## Slide 9: The 29 Industrial and Commercial Sectors, continued
Water Transportation Facilities with Vehicle Maintenance Shops and/or Equipment Cleaning Operations
Ship and Boat Building or Repair Yards
Vehicle Maintenance Areas, Equipment Cleaning Areas, or Deicing Areas Located at Air Transportation Facilities
Sewage treatment plants
Food and Kindred Products Facilities
Textile Mills, Apparel, and Other Fabric Products Manufacturing Facilities
Wood and Metal Furniture and Fixture Manufacturing Facilities
Printing and Publishing Facilities
Source: www.en.wikipedia.org/wiki/Industrial_stormwater

## Slide 10: The 29 Industrial and Commercial Sectors, continued
Rubber, Miscellaneous Plastic Products, and Miscellaneous Manufacturing Industries
Leather Tanning and Finishing Facilities
Fabricated Metal Products Manufacturing Facilities
Transportation Equipment, Industrial, or Commercial Machinery Manufacturing Facilities
Electronic and Electrical Equipment and Components, Photographic, and Optical Goods Manufacturing Facilities
Non-Classified Facilities
  Other industrial stormwater discharges designated by the Director as needing a permit, not classified as any previous Sector. (Assigned)
Source: www.en.wikipedia.org/wiki/Industrial_stormwater

## Slide 11: Requirements Regarding Site Inspections
EPA MSGP
OKR05 (Oklahoma MSGP)
Frequency of Inspections
Sector-Specific requirements
www.deq.ok.gov/water-quality-division/wastewater-stormwater/stormwater-permitting/okr05-industrial-stormwater/

## Slide 12: EPA MSGP
Both the current 2015 EPA Industrial MSGP and the proposed 2020 Industrial MSGP reflect the same requirements listed in the Oklahoma Industrial MSGP (OKR05).
For more information about the current and proposed EPA MSGPs:
www.epa.gov/npdes/stormwater-discharges-industrial-activities

## Slide 13: Requirements for Site Inspections - OKR05

## Slide 14: Requirements for Site Inspections - OKR05

## Slide 15: Frequency of Documented Site Inspections
Most facilities are required to document site inspections once per calendar quarter.
Always choose a site inspection frequency that will enhance your compliance with the requirements.
  For example, larger sites may benefit from more frequent inspections, especially if the yard is very active.
Depending on the business type or activity, more frequent site inspections may be required.
  Refer to the next several slides, documenting Sector-Specific site inspection requirements and frequencies. Not all sectors have additional requirements.

## Slide 16: Sector A: Timber Products
SIC Codes 2411, 2421, 2426, 2429, 2431 – 2439 (except 2434), 2441, 2448, 2449, 2451, 2452, 2491, 2493, 2499
Certain activities, monthly site inspections

## Slide 17: Sector D: Asphalt Paving & Roofing Materials & Lubricant Mfg.
SIC Codes: 2951, 2952, 2992, 2999
Monthly site inspections

## Slide 18: Sector F: Primary Metals
SIC Codes: 3312-3317, 3321-3325, 3331-3339, 3341, 3351-3357, 3363-3369, 3398, 3399
Quarterly site inspections, with documentation of specific areas and activities (as applicable to your site)

## Slide 19: Sector G: Metal Mining (Ore Mining and Dressing)
SIC Codes: 1011, 1021, 1031, 1041, 1044, 1061, 1081, 1094, 1099
Active mining sites: Monthly site inspections
  Inactive mining sites: Quarterly site inspections

## Slide 20: Sector H: Coal Mines & Coal Mining Related Facilities
SIC Codes: 1221, 1222, 1231, 1241
US Office of Surface Mining (OSM) – Surface Mining Control and Reclamation Act (SMCRA) requirements must be followed. Partial monthly site inspections & complete quarterly site inspections.
www.osmre.gov/lrg/docs/SMCRA.pdf

## Slide 21: Sector I: Oil & Gas Extraction
SIC Codes: 1321, 1389
Erosion & sediment controls, either:
  Weekly or
  Bi-weekly AND within 24 hours of 0.5” or greater rain event
Inactive sites must be inspected at least annually

## Slide 22: Sector J: Mineral Mining & Dressing
SIC Codes: 1411, 1422, 1423, 1429, 1442, 1446, 1455, 1459, 1474, 1475, 1479, 1481, 1499
Inspection frequencies vary, depending on site conditions.
  Activities prior to active mining: Bi-weekly AND within 24 hours of 0.5” or greater rain event.
  Monthly inspections for sites discharging to impaired waters.
  Otherwise, Quarterly unless inaccessible.

## Slide 23: Sector L: Landfills, Land Application Sites & Open Dumps
Activity Code: LF
Inspection frequencies vary, depending on site conditions.
  New cells: Bi-weekly AND within 24 hours of 0.5” or greater rain event.
  Active sites: weekly.

## Slide 24: Sector M: Automobile Salvage Yards
SIC Code: 5015
Inspect arriving vehicles immediately.
Site inspections: Quarterly
Final inspection of site before filing an NOT to terminate coverage.

## Slide 25: Sector N: Scrap Recycling Facilities
SIC Code: 5093
Quarterly inspections, with special attention to specific areas.

## Slide 26: Sector O: Steam Electric Generating Facilities
Activity Code: SE
Monthly inspections, with special attention to specific areas.

## Slide 27: Sector P: Land Transportation & Warehousing
SIC Codes: 4011, 4013, 4111-4173, 4212-4231, 4311
Quarterly inspections, with special attention to specific areas.

## Slide 28: Sector Q: Water Transportation
SIC Codes: 4412-4499
Quarterly inspections, with special attention to specific areas.

## Slide 29: Sector R: Ship and Boat Building or Repairing Yards
SIC Codes: 3731, 3732
Quarterly inspections, with special attention to specific areas.

## Slide 30: Sector S: Air Transportation
SIC Codes: 4512, 4513, 4522, 4581
Weekly inspections during deicing season
  Otherwise, quarterly inspections

## Slide 31: Sector T: Treatment Works
Activity Code: TW
Quarterly inspections, with special attention to specific areas.

## Slide 32: Sector U: Food & Kindred Products
SIC Codes: 2011-2015, 2021-2026, 2032-2038, 2041-2048, 2051-2053, 2061-2068, 2074-2079, 2082-2087, 2091-2099, 2111-2141
Quarterly inspections, with special attention to specific areas.

## Slide 33: Sector V: Textile Mills, Apparel & Other Fabric Product Mfg., Leather & Leather Products
SIC Codes: 2211-2299, 2311-2399, 3131-3199
Monthly inspections, with special attention to specific areas.

## Slide 34: Sector AA: Fabricated Metal Products
SIC Codes: 3411-3499, 3911-3915
Quarterly inspections, with special attention to specific areas.

## Slide 35: Site Inspection Documentation
DEQ templates can be found here:
www.deq.ok.gov/water-quality-division/wastewater-stormwater/stormwater-permitting/okr05-industrial-stormwater

## Slide 36: DEQ Reports Templates

## Slide 37: Routine Facility Inspection Report – page 1
The Business – OKC Office
OKR059999/SWI-2015-00352
01/15/2017
9:15am
10:15am
Mr. Team Leader
EHS Coordinator, 405-797-3546

## Slide 38: Routine Facility Inspection Report – page 1
73 o F
0.47”
Slow, steady rain since 3am, runoff appears clear and clean.

## Slide 39: Routine Facility Inspection Report – page 1
Need to sweep up metal shavings

## Slide 40: Routine Facility Inspection Report – page 2

## Slide 41: Routine Facility Inspection Report – page 2
Metal pipe racks, stock material

## Slide 42: Routine Facility Inspection Report – page 2
Metal awning
Compost soxx

## Slide 43: Routine Facility Inspection Report – page 3
If you have more Structural BMPs, inspect and list them here!

## Slide 44: Routine Facility Inspection Report – page 3
Outfall appears clean, stable, and flowing efficiently.

## Slide 45: Routine Facility Inspection Report – page 4
Metal shavings need cleaned up around
scrap bin. Employees state that incident occurred during bin swapout. Need to check area daily.
No additional controls needed.

## Slide 46: Routine Facility Inspection Report – page 4
Mr. Team Leader
EHS Coordinator
01/15/2017
Mr. Team Leader
No other notes/observations at this time.

## Slide 47: General Guideline for Site Inspections
Always available on your Workshop CD’s,
or ask your inspector for a copy

## Slide 48: Available on Workshop CDs

## Slide 49: Available on Workshop CDs
General Guideline for Site Inspections, continued:

## Slide 50: Site Examples of What to Look For
(These are also things Regulators look for)

## Slide 51: Loading & Unloading Areas
Spills, leaks, drips & trash accumulations

## Slide 52: Materials Handling
Spills, leaks, drips & trash accumulations
Other concerns?

## Slide 53: Vehicles & Equipment: Parking & Storage Areas
Spills, leaks, drips & trash accumulations
Exposed oil/grease/mud/dirt
Potential for leaks (drain fluids or use drip pans)

## Slide 54: Materials Storage Areas
Spills, leaks, drips & trash accumulations
Deterioration of containers
  Open, rusted, dented must be covered
Containers elevated, closed, covered
Clean, neat and tidy work areas are best!

## Slide 55: Trash, Scrap & Recycling Containers
Operational, closed lids
Drain plug, leakproof (not rusted out), covered

## Slide 56: Outdoor Surfaces & Fence Lines
Spills, leaks, drips & trash accumulations

## Slide 57: Chemical Storage
Secondary containment on tanks
Spills, leaks, drips & trash accumulations
Deterioration of containers
  Rusted, dented must be covered
Containers elevated, closed, covered
Spill kits nearby

## Slide 58: Best Practices & Controls
Operational, functional, in place
Appropriate, sufficient?

## Slide 59: Outfall Areas
General condition, trash accumulation
Sheen, foam, sedimentation/erosion

## Slide 60: Record Retention

## Slide 61: Record Retention
From the OKR05:
  Keep all records at least 3 years from the date that your permit coverage expires or is terminated.

## Slide 62: DEQ FAQ’s
Routine Facility Inspection
www.deq.ok.gov/water-quality-division/wastewater-stormwater/stormwater-permitting/okr05-industrial-stormwater/

## Slide 63: Routine Facility Inspection – DEQ FAQ’s
www.deq.ok.gov/water-quality-division/wastewater-stormwater/stormwater-permitting/okr05-industrial-stormwater/

## Slide 64: Routine Facility Inspection – DEQ FAQ’s
www.deq.ok.gov/water-quality-division/wastewater-stormwater/stormwater-permitting/okr05-industrial-stormwater/

## Slide 65: Routine Facility Inspection – DEQ FAQ’s
www.deq.ok.gov/water-quality-division/wastewater-stormwater/stormwater-permitting/okr05-industrial-stormwater/

## Slide 66: Routine Facility Inspection – DEQ FAQ’s
www.deq.ok.gov/water-quality-division/wastewater-stormwater/stormwater-permitting/okr05-industrial-stormwater/

## Slide 67
For more information: www.okc.gov/SWQ
www.deq.ok.gov
www.epa.gov
Questions? email: rebecca.dallen@okc.gov
Notes: Image credit: Getty Images